## Slide 1
SENSORED 9.0
ESP32 INTRO

## Slide 2
ESP8266-01
ESP8266
ESP - 32

## Slide 3
ESP 32
The ESP-32 is a microcontroller chip developed by Espressif Systems.

## Slide 4
ABOUT ESP 32
  With the ESP-32, you can control inputs and outputs as you would do with an Arduino, but with Wi-Fi and Bluetooth capabilities.
  Can generate its own Wi-Fi network (access point) or connect to other Wi-Fi networks (station) to get access to the internet.
  Access point mode: It can create its own Wi-Fi network to which other devices can connect ( eg. Other ESP-32 , Mobile etc.) .
  Station mode: It can be connected to any Wi-fi or Mobile hotspot.

## Slide 5
IoT

## Slide 6
PIN DIAGRAM

## Slide 8
PIN DIAGRAM
GPIO – General purpose I/O pin (25 Pins)
Vcc – Power supply ( 3.3V)
GND – Ground
Tx – Transmit pin for Serial Communication
Rx – Receiver pin for Serial Communication
EN – Chip enable pin. It must be pulled high (connected to VCC) for the module to function properly.
Reset pin – Resets the entire board.

## Slide 9
SPECIFICATION
Power Supply: +3.6V only
Current Consumption: 100mA
I/O Voltage: 3.6V (max)
I/O current: 12mA (max)
Maximum data rate of up to 5 Mbps
ROM: 448 Kbyte
RAM: 520 KByte
Operates in 2.4 GHz , 5 GHz frequency band
Uses UART ,I2C ,SPI ,I2S protocols for data exchange

## Slide 10
WHY ESP-32?
Can even go into deep sleep mode to consume less power.
ESP-32 can access online services to make HTTP requests or save data to the cloud.
you can access it using a web browser and be able to control and monitor your boards remotely.
Compatible with Arduino programming language and MicroPython which is a re-implementation of Python specially targeted for microcontrollers and embedded system.

## Slide 11
INSTALLATION URL
https://dl.espressif.com/dl/package_esp32_index.json

## Slide 12
BOARD INSTALLATION PROCESS
STEP 1
STEP 2

## Slide 13
BOARD INSTALLATION PROCESS
STEP 3
STEP 4

## Slide 14
BOARD INSTALLATION PROCESS

## Slide 15
Presented by
Sathish Sarathy