## Slide 1
SENSORED 9.0
IR SENSORS

## Slide 2
Let’s START the Theoretical basics of the
IR sensor !!!

## Slide 3
Parts of an IR Sensor
Receiver photodiode
LED
Data Pin
Ground
pin
5V collector current
pin
Sensitivity
Manipulator
LM393 IC

## Slide 4
PARTS OF THE IR LED
Long lead ---- Anode (+)
Short lead --- Cathode (-)

## Slide 5
PHOTODIODE
Long lead ---- Anode (+)
Short lead --- Cathode (-)
Absorb the radiation  Photocurrent generation Conversion to voltage

## Slide 6
Why is the photodiode black ?

## Slide 7
DUAL DIFFERENTIAL COMPARATOR(LM393)
Received Voltage > Reference Voltage : Outputs the signal
Else : Ignores the object

## Slide 8
Potentiometer
Clockwise : Increase reference voltage
Counter clockwise : Decrease reference voltage

## Slide 9
CONNECTING PINS

## Slide 10
Theory of IR Sensor

## Slide 11
Parts of an IR Sensor
Receiver photodiode
LED
Data Pin
Ground
pin
5V collector current
pin
Sensitivity
Manipulator
LM393 IC

## Slide 12
Any doubts guys?

## Slide 13
You Buy a product only if it’s useful to you in some way or the other.
So let’s discuss the real-life applications of the IR Sensor…

## Slide 14
Automatic door
Automatic soap dispenser
Do you know how these work?

## Slide 15
drawbacks
Unreliable in ambient conditions
Penetration power and low frequency
Drawbacks of IR Sensor
Unreliable in environmental conditions
IR ray at high power can damage your eyes
IR region is very small (700-1000nm)
Sensor range is very low
If the object is black then the IR sensor module might not
sense it.

## Slide 16
Unreliable in ambient conditions
Penetration power and low frequency
Projects using IR sensor
Any creative ideas?

## Slide 17
Interesting projects
Black line following robot
IR contactless bell
Traffic signal project:

## Slide 18
Interesting projects
Black line following robot
IR contactless bell
Vehicle speed detector project:

## Slide 19
Interesting projects
Vehicle speed detector project:

## Slide 20
ARE YOU GUYS READY FOR THE CODING AND HANDS ON PART ???

## Slide 21
CODE
.
#define SENSOR_PIN 18
void setup() {
Serial.begin(9600); //This initializes the serial communication at a baud rate of 9600 bits per second.
pinMode(SENSOR_PIN, INPUT); //sets SENSOR_PIN(pin 18) as input
}
void loop() {
int state = digitalRead(SENSOR_PIN); //reads the value from SENSOR_PIN
if (state == HIGH)
Serial.println("The obstacle is present");
else
Serial.println("The obstacle is NOT present");
delay(100); //introduces a delay of 100 milliseconds between consecutive sensor readings
}
}

## Slide 22
READY FOR THE CONNECTIONS SEGMENT?

## Slide 24
THANK YOU

## Slide 25
Speaker
Devadarsh Prakash